## Slide 1
Project Partner SGS – GeoSolutions, Belgrade
Vladimir Bulatovic
An AI/IOT-based system of GEOsensor NETworks for real-time monitoring of unStablE tErrain and artificial structures ---GNSS sensors, data and processing---

## Slide 2
ToC
GNSS sensors
Precise GNSS technique
Node Network and connectivity
Solutions of GeoSolutions

## Slide 3
gps+glo+gal+bei
2+ frequency
Code and carrier phase observables
1hz data output
RTK engine on board
Survey antenna
LNA
APC high stability ~2mm
Basic GNSS sensor requirements

## Slide 4
Precise GNSS technique
Dominant systematic errors (time synchronization, ionospheric delay, tropospheric delay)
Relative positioning
  RTK
  PPK
  Network of static baselines

## Slide 5
RTK
2-3cm accuracy
Results available in Real-Time

## Slide 6
PPK
<1cm accuracy
Results available after processing on daily basis
Specialized software required

## Slide 7
Network of static baselines
3-4mm horizontal accuracy, 5-7mm vertical accuracy
Require more baselines than unknown point
LSA provide quantity and quality evaluation
Several gnss must be on stable locations
Daily results within same coordinate system build time series

## Slide 8
Node network and connectivity
NTRIP protocol
  Protocol for streaming GNSS data over the internet. NTRIP protocol is based on Hypertext Transfer Protocol HTTP/1.1
  NTRIP is agnostic and can be used for other sensors
  NTRIP has 3 components (client, server and caster)

## Slide 9
GeoSolutions solutions
GNSS CORS network
GNSS CORS stations
GSCaster2
Analytics

## Slide 10
GeoSolutions solutions Regional CORS network
45 CORS stations
>250 Clients

## Slide 11
GeoSolutions solutions CORS station
gps+glo+bei+gal
3 frequencies
5V
RJ45, WIFI, serial
RTCM and ASCII output
Ntrip client/server
Modular

## Slide 12
GeoSolutions solutions GSCaster2
Specifications
Written in C programming language
GNSS data broadcast in real-time over the Internet using the ntrip dissemination technique
Running on LINUX (tested for various distributions, such as SuSE, Debian, Gentoo, Redhat)
Supporting ntrip versions 1 and 2
Logging RINEX files or check their quality;
Decoding RTCM Version 3 'Multiple Signal Messages' (MSM) and 'High Precision Multiple Signal Messages' (HP MSM) including X-type observations for GPS, GLONASS and Galileo;
Easy installation and configuration based on a low number of configuration files
Tested for more than 100 data streams and more than 2000 simultaneous users

## Slide 13
GeoSolutions solutions Analytics
RTK, PPK, Network adjustment, PPP
Internet communication
IoT networks

## Slide 14
GentooARS – GeoSolutions core business
http://geosolutions.co.rs:2101/admin